## Slide 1: A 40m XTAL Transceiver For £20
Based on Homebrew Kits
G4FVZ

## Slide 2: The Stable So far:

## Slide 3: Low Cost ‘HAM’ Kits
Sourced from China and Hong Kong
  Ebay
  Amazon
  BangGood
Most of the time postage is free and customs duty under limit
Found to reliable in delivery – usually no more than 2 weeks
Chinese copies of US kits costing substantially more
Can be built as modules

## Slide 4: But Buyer Beware!
Component quality is sometime doubtful
Some components not labelled
Components occasionally missing – usually they use a ‘handful’ approach
Companies have customer service – missing components – it works
Component boards are good quality but are sometime ‘changed’ from original
  Frog kit spoilt by mark V board
Inexpensive so sometimes ordering two for back up
Instruction limited- some English , some Chinese
Some components e.g. PA transistors probably ’not original’
  Stock of driver transistors and PA transistors

## Slide 5: Test everything !
Test every component thoroughly
Mark as you go – circuit diagram and component list
Remember 2-2-2
PCB Boards double sided
Errors are difficult to correct once soldered
Try and socket the PA transistor – may need to change it
Heat sink the PA transistor
Don’t mix up the key and phones socket
Remember the dummy load

## Slide 6: Starting Point THE PIXIE £2.50
40m CW Transceiver
Crystal controlled on RX and TX (7.023)
No coils/torroids!
Some bandpass 2-3KHZ
A couple of watts – variable (0.5W)
Only drive headphones
Start up from fresh PP3 but 12V PSU
Only like to see 50Ω

## Slide 7: Moving From The PIXIE To 49-er
£7.20
More power 2-3 W (0.5W more typical)
Still only drives headphones
Still Xtal controlled
  One for LO of RX/TX other for receiver front end filter
CW sidetone
Works reasonably well
Care with torroids T-37-2 is red!
Hissy

## Slide 8: Forty-9er Circuit As Supplied

## Slide 9: Moving ON TO RM-80 (super Rockmite)
Now up to 8W (5W)
PIC Keyer
Dense board
Circuit at limit (oscillastion)
4 torroids -2 transformers
Still only headphones output
£13
Could form the basis of transceiver
Super RM yahoo group
Can bypass keyer

## Slide 10: What needs to be added?
Audio to drive speaker - ~£1- 2
Some preassembled, some kit
Fitted in same enclosure as 49-er/RM80
{Review quality of LM386}

## Slide 11: And BPF
Make from G-QRP club
40M design
Cost about £1.50 using veroboard

## Slide 12: And finally a case
Chinese source
  Aluminum or ABS
About £5

## Slide 13: Final tally
49 –er £7.30 RM80 £13.50
Audio £2.50 Audio £ 2.50
LPF £2.00 LPF £ 2.00
Case £5.00 Case £ 7.00
£16.80
£25

## Slide 14: Examples At G4FVZ : 49-er

## Slide 15: Examples At G4FVZ : RM 80

## Slide 16: Frog Kit: Beware!
Pig to get going
Board changed and doesn’t match circuit diagram – R19 conundrum
Component quality particularly bad – PA transistor arrived in two pieces!
Driver and PA transistor changed to get output
US seemed to have more success

## Slide 17: Summary : Pros and Cons
Can be built for £20 ; £25 if higher power/keyer
Project costs comes down with volume
Relatively easy homebrew project
No real major set up – multi-meter, component analyser, frequency meter
It works – CW QSO’s
But XTAL controlled – VFO?

## Slide 18: Getting more Frequency Coverage : see KC9on.com

## Slide 19: Linking A 49-Er to a DDS just out in Mar 2016 QST!

## Slide 20: QST Article Shows How to MAKE LINK
All sourced from Ebay, Amazon etc
Uses Arduino nano, DDS module and LCD display
Additional parts – £12
Needs bigger case
Full TCR - £30?

## Slide 21: Club Project?
Start with 49-er?
    Take bandpass as external control
    Socket up the PA transistor
    Consider buying better PA transistors
    Build a 20m variant
Transition it into a 40M DDS Arduino 49-er CW Transceiver
Gain volume of scale to reduce cost
Buildathon day?
Needs commitment of £25 per person

## Slide 22: A 40m DDS VFO Transceiver For £20 £25
Based on Homebrew Kits