## Slide 1: Putting up a 40m Dipole –Practical Considerations
G3TZO

## Slide 2: Current Antennas – Butternut HF6V
80,40,30,20,15 & 10m
Height 26 ft.
Rated 1.5KW
Uses a 75Ω matching line to 50Ω coax

## Slide 3: TET EMTRON TE33M HF Beam

## Slide 4: TET EMTRON TE33M HF Beam
20m 15m & 10m
Max Element 5.5m
Boom 4.0m
6/6/7 dBi
F/B Ratio 20,15 & 14dB
Impedance 50Ω
Turning radius 3.74m

## Slide 5: Anticipated advantages of a 40m Dipole
Lower noise floor on 40m
Higher angle radiation
Better daytime UK coverage
Single band antenna

## Slide 6: Practical Considerations
Where to put it

## Slide 7: Location

## Slide 8: Practical Considerations
Where to put it
How to fix the two ends

## Slide 9: South end

## Slide 10: North end

## Slide 11: Practical Considerations
Where to put it
How to fix the two ends
What wire to use

## Slide 12: Dark Green Heavy Duty Antenna Wire from SOTABEAMS
Specification
1,000 Watts RF rated (50Ω)
conforms to Military Defence Standard 61-12 pt 6,
tinned annealed copper conductor,
1 mm² total conductor CSA (approx. 17AWG)
32 strands x 0.2 mm copper conductor stranding,
2.55 mm cable diameter,
Voltage Rating: 1.5 kV rms,
PVC insulation,
Weight 750 g/50 m (approx. 15 g/metre),
Insulation colour: Green,
Current Rating: 10 A at 25 °C,
Resistance: less than 1 Ohm per 50 metres
Velocity factor 0.97

## Slide 13: Practical Considerations
Where to put it
How to fix the two ends
What wire to use
How to fix it to the mast

## Slide 15: HEAVY DUTY PULLEY
Used with 8mm Round Polypropylene Rope

## Slide 16: Practical Considerations
Where to put it
How to fix the two ends
What wire to use
How to fix it to the mast
How to terminate the antenna

## Slide 17: Centre Termination
Homebrew (3D etc)
Simple feed point
Balun

## Slide 18: MFJ-918 Balun
Designed to replace the centre insulator
Constructed of 50 ferrite core beads placed on a 13-inch length of RG-303 coax
Direct electrical connections to the antenna with #14 copper wire
Top support to halyard

## Slide 19: 50Ω Feeder via 1:1 Balun

## Slide 20: Practical Considerations
Where to put it
How to fix the two ends
What wire to use
How to fix it to the mast
How to terminate the antenna
Routing into the shack

## Slide 21: RG213 Cable Routing

## Slide 22: RG213 Cable Routing

## Slide 23: Practical Considerations
Where to put it
How to fix the two ends
What wire to use
How to fix it to the mast
How to terminate the antenna
Routing into the shack
Switching considerations

## Slide 24: Ameritron RCS4

## Slide 25: Switching

## Slide 26: Dust Covers Fitted

## Slide 27: Cutting to length (everythingrf.com)

## Slide 28
Testing using the Nano Vna

## Slide 33
SUCCESS !!

## Slide 34: MMAN-GAL Plot

## Slide 36: Planned spring enhancements

## Slide 37: Planned spring enhancements
For clamping wire firmly at each insulator

## Slide 38: Planned spring enhancements

## Slide 39: Tidy up pulley rope

## Slide 40: Specialist suppliers of antenna bits
Mastrant (Czech Republic)
https://www.mastrant.com/
HF Kits (Nederlands)
https://www.hfkits.com/
M0MAT RF Devices (UK)
https://www.ebay.co.uk/str/m0mat
Plus the usual Amateur dealers such as Moonraker etc.

## Slide 41: Reference Material
Antennas – General
RSGB & ARRL Handbooks
RSGB Book Shop – HF Antennas For Everyone Giles Read G1MFG
Internet – Best for antenna such as the ZS6BKW
YouTube – Mostly helpful sometimes confusing
Classics – HF Antennas for all locations Les Moxon G6XN
The list goes on.